## Slide 1: DHCPv6

## Slide 2: Stateful DHCPv6
In Stateful DHCP, the adddress assignment is centrally managed and clients must obtain configuration information such as address autoconfiguration and neighbor discovery that is not available through protocols.
DHCPv6 can be implemented in two ways
  Rapid Commit - DHCP client obtains configuration parameters from the server through a rapid two message exchange (solicit and reply).
  Normal Commit - DHCP client uses four message exchanges (solicit, advertise, request and reply).
By default normal-commit is used.
In order to use the rapid-commit option, it has to be enabled by both client and server so that it uses the two-message exchange.

## Slide 3: Stateless Address Autoconfiguration (SLAAC)
Requires no manual configuration of hosts, minimal (if any) configuration of routers, and no additional servers.
DHCP clients autoconfigure their own IPv6 address based on router advertisements. Routers advertise prefixes that identify the subnet(s) associated with a link, while hosts generate an "interface identifier" that uniquely identifies an interface on a subnet.
DHCP clients uses the DHCP server to obtain the other useful configuration information (such as the address of DNS servers).
By using the eui-64 command, a host can automatically assign itself a unique 64-bit IPv6 interface identifier without the need for manual configuration or DHCP.
This approach is used when a network is not concerned with the exact addresses hosts use on a network so long as they are unique and routable.

## Slide 4: DHCPv6 Message Types
DHCPv6 Message Types | DHCPv4 Message Types
SOLICIT(1) | DHCPDISCOVER
ADVERTISE(2) | DHCPOFFER
REQUEST (3), RENEW (5), REBIND (6) | DHCPREQUEST
REPLY (7) | DHCPACK/DHCPNAK
RELEASE (8) | DHCPRELEASE
INFORMATION-REQUEST (11) | DHCPINFORM
DECLINE (9 | DHCPDECLINE
CONFIRM (4) | None
RECONFIGURE (10) | DHCPFORCERENEW
RELAY-FORW (12), RELAY-REPLY (13) | None
Used to locate DHCP Servers
Sent by servers to indicate that it is available for DHCP service.
Sent by hosts to request addressing information from the server, renew an old IP address and extend the lifetime of an address.

## Slide 5: DHCPv6 Message Types
DHCPv6 Message Types | DHCPv4 Message Types
SOLICIT(1) | DHCPDISCOVER
ADVERTISE(2) | DHCPOFFER
REQUEST (3), RENEW (5), REBIND (6) | DHCPREQUEST
REPLY (7) | DHCPACK/DHCPNAK
RELEASE (8) | DHCPRELEASE
INFORMATION-REQUEST (11) | DHCPINFORM
DECLINE (9 | DHCPDECLINE
CONFIRM (4) | None
RECONFIGURE (10) | DHCPFORCERENEW
RELAY-FORW (12), RELAY-REPLY (13) | None
Sent by the server containing address configuration.
Sent by hosts to indicate that the host will no longer use an address.
Sent by hosts to request configuration parameters without the assignment of any address to the client.
Sent by hosts to deny updates sent from the server.
Sent by the server to inform clients of changes in addressing configuration.

## Slide 6: DHCPv6 Messages Types
There are 3 DHCPv6 message types exclusive to only DHCPv6:
  - CONFIRM (4)
  A client sends a Confirm message to any available server to determine whether the addresses it was assigned are still appropriate to the link to which the client is connected.
  - RELAY-FORW (12)
  A relay agent sends a Relay-forward message to relay messages to servers, either directly or through another relay agent.
  - RELAY-REPL (13)
  A server sends a Relay-reply message to a relay agent containing a message that the relay agent delivers to a client.

## Slide 7: Stateful DHCPv6 Server Configuration Example 1
The ipv6 dhcp pool command creates a pool and enters the router in DHCPv6 configuration mode.
The address command is used to indicate the pool of addresses to be allocated by the server. The lifetime option indicates the valid and preferred lease times in seconds.
The ipv6 dhcp server interface command binds the DHCPv6 pool to the interface.
The M flag needs to be changed from 0 to 1 using the interface command ipv6 nd managed-config-flag.
R2
S0/0/0
R1
2001:DB8:ACAD:1::/64
S0/0/0
Client
Server
Link-Local FE80::1
Link-Local FE80::2

## Slide 8: Stateful DHCPv6 Server Configuration
R1(config)#ipv6 unicast-routing
R1(config)#ipv6 dhcp pool Stateful_DHCP
R1(config-dhcpv6)#address prefix 2001:DB8:acad:1::/64 lifetime infinite infinite
R1(config-dhcpv6)#dns-server AAAA:BBBB:CCCC:DDDD::FFFF
R1(config-dhcpv6)#domain-name StatefulDHCP.com
R1(config-dhcpv6)#exit
R1(config)#interface s0/0/0
R1(config-if)#ipv6 address 2001:db8:acad:1::1/64
R1(config-if)#ipv6 dhcp server Stateful_DHCP
R1(config-if)#ipv6 nd managed-config-flag
R2
S0/0/0
R1
2001:DB8:ACAD:1::/64
S0/0/0
Client
Server
Link-Local FE80::1
Link-Local FE80::2
Notes: Configuration parameters to configure a router as a DHCP server.

## Slide 9: Stateful DHCPv6 Client Configuration
The ipv6 enable interface command allow the router to receive a link-local address in order to send RS messages and participate in DHCPv6.
The ipv6 address dhcp interface command enables the router as a DHCPv6 client on this interface.
R2(config)#interface s0/0/0
R2(config-if)#ipv6 enable
R2(config-if)#ipv6 address dhcp
R2
S0/0/0
R1
2001:DB8:ACAD:1::/64
S0/0/0
Client
Server
Link-Local FE80::1
Link-Local FE80::2
Notes: Configuration to allow a router to act as a DHCP client.

## Slide 10: Stateful DHCPv6 Server Verification
R1#show ipv6 dhcp pool
DHCPv6 pool: Stateful_DHCP
Address allocation prefix: 2001:DB8:ACAD:1::/64 valid 4294967295 preferred 4294967295 (1 in use, 0 conflicts)
DNS server: AAAA:BBBB:CCCC:DDDD::FFFF
Domain name: StatefulDHCP.com
Active clients: 1
R1#show ipv6 dhcp binding
Client: FE80::2
DUID: 000300016C2056EC6F18
Username : unassigned
IA NA: IA ID 0x00070001, T1 43200, T2 69120
Address: 2001:DB8:ACAD:1:2CFA:91CC:C683:D1F5
preferred lifetime INFINITY, , valid lifetime INFINITY,
The show ipv6 dhcp pool command verifies the name of the DHCPv6 pool and its parameters. The number of active clients is 1, which reflects client R2 receiving its IPv6 global unicast address from this server.
The show ipv6 dhcp binding command, displays the automatic binding between the link-local address of the client and the address assigned by the server.

## Slide 11: Stateful DHCPv6 Client Verification
R2#show ipv6 dhcp interface
Serial0/0/0 is in client mode
Prefix State is IDLE
Address State is OPEN
Renew for address will be sent in 11:59:44
List of known servers:
Reachable via address: FE80::1
DUID: 000300016C2056FF38A0
Preference: 0
Configuration parameters:
IA NA: IA ID 0x00070001, T1 43200, T2 69120
Address: 2001:DB8:ACAD:1:B0A4:64F:CA3F:FA2D/128
preferred lifetime INFINITY, valid lifetime INFINITY
DNS server: AAAA:BBBB:CCCC:DDDD::FFFF
Domain name: StatefulDHCP.com
Information refresh time: 0
Prefix Rapid-Commit: disabled
Address Rapid-Commit: disabled
R2
S0/0/0
R1
2001:DB8:ACAD:1::/64
S0/0/0
Client
Server
Link-Local FE80::1
Link-Local FE80::2
Notes: The show ipv6 dhcp interface command displays the interfaces that were configured via DHCP. It also displays the link-local address of the DHCP server.

## Slide 12: DHCPv6 Configuration Example 2
R2
S0/0/0
R1
2001:DB8:ACAD:1::/64
S0/0/0
Client
Server
Link-Local FE80::1
Link-Local FE80::2
DHCP Host
R1(config)#ipv6 unicast-routing
R1(config)#ipv6 dhcp pool MY_DHCP_POOL
R1(config-dhcpv6)#address prefix 2001:DB8:cc1e:1::/64 lifetime infinite infinite
R1(config-dhcpv6)#dns-server AAAA:BBBB:CCCC:DDDD::FFFF
R1(config-dhcpv6)#domain-name HOSTdhcp.com
R1(config-dhcpv6)#exit
R1(config)#interface g0/0
R1(config-if)#ipv6 address 2001:db8:cc1e:1::/64
R1(config-if)#ipv6 dhcp server MY_DHCP_POOL
R1(config-if)#ipv6 nd managed-config-flag

## Slide 13: DHCPv6 Host Verification
R2
S0/0/0
R1
2001:DB8:ACAD:1::/64
S0/0/0
Client
Server
Link-Local FE80::1
Link-Local FE80::2
DHCP Host

## Slide 14: Stateless DHCPv6
During the SLAAC process, the client receives information to create an IPv6 global unicast address. This includes the default gateway information from the source IPv6 address in the RA message, which is the link-local address of the router. A stateless DHCPv6 server can be used to provide information that might not be included in the RA message (DNS server address and the domain name).
The ipv6 dhcp server interface command binds the DHCPv6 pool to the interface.
The O flag needs to be changed from 0 to 1 using the interface command ipv6 nd other-config-flag.
R2
S0/0/0
R1
2001:DB8:ACAD:1::/64
S0/0/0
Client
Server
Link-Local FE80::1
Link-Local FE80::2
Notes: Using the same topology, we will configure stateless DHCP servers and clients.

## Slide 15: Stateless DHCPv6 Server Configuration
R2
S0/0/0
R1
2001:DB8:ACAD:1::/64
S0/0/0
Client
Server
Link-Local FE80::1
Link-Local FE80::2
R1(config)#ipv6 unicast-routing
R1(config)#ipv6 dhcp pool Stateless_DHCP
R1(config-dhcpv6)#dns-server AAAA:BBBB:CCCC:DDDD::FFFF
R1(config-dhcpv6)#domain-name StatelessDHCP.com
R1(config-dhcpv6)#exit
R1(config)#interface s0/0/0
R1(config-if)#ipv6 address 2001:db8:acad:1::1/64
R1(config-if)#ipv6 dhcp server Stateless_DHCP
R1(config-if)#ipv6 nd other-config-flag

## Slide 16: Stateless DHCPv6 Client Configuration
R2
S0/0/0
R1
2001:DB8:ACAD:1::/64
S0/0/0
Client
Server
Link-Local FE80::1
Link-Local FE80::2
R2(config)#interface s0/0/0
R2(config-if)#ipv6 enable
R2(config-if)#ipv6 address autoconfig
The ipv6 enable command is used because the router does not have a global unicast address.
The ipv6 address autoconfig command enables automatic configuration of IPv6 addressing using SLAAC.

## Slide 17: Stateless DHCPv6 Verification
R2#show ipv6 interface s0/0/0
Serial0/0/0 is up, line protocol is up
IPv6 is enabled, link-local address is FE80::2
No Virtual link-local address(es):
Stateless address autoconfig enabled
Global unicast address(es):
2001:DB8:ACAD:1::2, subnet is 2001:DB8:ACAD:1::/64 [EUI/CAL/PRE]
valid lifetime 2591259 preferred lifetime 604059
Joined group address(es):
FF02::1
FF02::1:FF00:2
MTU is 1500 bytes
ICMP error messages limited to one every 100 milliseconds
ICMP redirects are enabled
ICMP unreachables are sent
ND DAD is enabled, number of DAD attempts: 1
ND reachable time is 30000 milliseconds (using 30000)
ND RAs are suppressed (periodic)
Hosts use stateless autoconfig for addresses.
Notes: The show ipv6 interface command shows that the router has “Stateless address autoconfig enabled” and has an IPv6 global unicast address (2001:DB8:ACAD:1::2) and displays the subnet address (2001:DB8:ACAD:1::/64) as well. The IPv6 global unicast address was created using SLAAC which includes the prefix contained in the RA message. The Interface ID was generated using EUI-64 which is displayed to the right of the subnet address. The Duplicate Address Detection (DAD) is used to verify no one else on the network is using the address that you created.