## Slide 1: IPv6 EIGRP
John Rullan Cisco Certified Instructor Trainer Thomas A. Edison CTE HS Stephen Lynch
Network Architect, CCIE #36243
ABS Technology Architects

## Slide 2: Topology
Branch-2
2001:DB8:ACAD:C::2/64
2001:DB8:CAFE::/127
2001:DB8:ACAD:C::1/64
S0/0/0
S0/0/1
Branch-3
S1
S2
Branch-1
2001:DB8:CAFE::2/127
S3
S4
PC-A
PC-B
PC-C
PC-D
2001:DB8:ACAD:D::1/64
2001:DB8:ACAD:A::1/64
2001:DB8:ACAD:B::1/64
S0/0/1
S0/0/0
2001:DB8:ACAD:D::2/64
2001:DB8:ACAD:A::2/64
2001:DB8:ACAD:B::2/64
Lo0 2001:DB8:1::/64

## Slide 3: Configuring IPv6 EIGRP on a Network
IPv6 packet forwarding is disabled by default. To enable IPv6 packet forwarding, use the ipv6 unicast-routing command in global configuration mode before enabling EIGRP.
A router ID is mandatory for IPv6 EIGRP to be functioning properly. If one isn't manually configured, one will be generated using the loopback or physical interface.
Branch-1(config)# ipv6 router eigrp 100
% IPv6 routing not enabled
Branch-1(config)# ipv6 unicast-routing
Branch-1(config)# ipv6 router eigrp 100
Branch-1(config-rtr)# router-id 1.1.1.1
Branch-1(config-rtr)# no shutdown
Branch-1(config)# ipv6 router eigrp 100
Branch-1(config-rtr)# eigrp router-id 1.1.1.1
Packet Tracer
Real Equipment

## Slide 4: Configuring IPv6 EIGRP on a Network
Unlike IPv4 EIGRP, IPv6 EIGRP does not require the use of network command to advertise its networks. Instead IPv6 EIGRP must be enabled on all of the router's interfaces.
This command must be configured on all of the router's interfaces that are participating in EIGRP. If we fail to configure this command on an interface, that network will not be advertised, therefore, will not be learned by its neighbors.
Branch-1(config)# int s0/0/0
Branch-1(config-if)# ipv6 eigrp 100
Branch-1(config-if)# int g0/0
Branch-1(config-if)# ipv6 eigrp 100
Branch-1(config-if)# int g0/1
Branch-1(config-if)# ipv6 eigrp 100

## Slide 5: Configuring IPv6 EIGRP on a Network
When IPv6 EIGRP is configured on all interfaces, a log message will inform you that an adjacency has formed.
Branch-2(config)# int s0/0/0
Branch-2(config-if)# ipv6 eigrp 100
Branch-2(config-if)#
%DUAL-5-NBRCHANGE: IPv6-EIGRP 100: Neighbor FE80::1 (Serial0/0/0) is up: new adjacency
Branch-2(config-if)# int s0/0/1
Branch-2(config-if)# ipv6 eigrp 100
Branch-2(config-if)#
%DUAL-5-NBRCHANGE: IPv6-EIGRP 100: Neighbor FE80::3 (Serial0/0/1) is up: new adjacency
Branch-2(config-if)#

## Slide 6: IPv6 Show Commands
Neighbor’s IPv6
Link-local Address
Local Interface
receiving EIGRP for IPv6 Hello packets
Seconds remaining before declaring neighbor down.
The current hold time and is reset to the maximum hold time whenever a Hello packet is received.
Amount of time since this neighbor was added to the neighbor table.
Branch-2# show ipv6 eigrp neighbor
IPv6-EIGRP neighbors for process 100
H Address Interface Hold Uptime SRTT RTO Q Seq
(sec) (ms) Cnt Num
0 Link-local address: Se0/0/0 14 00:01:31 40 1000 0 18
FE80::1
1 Link-local address: Se0/0/1 12 00:01:24 40 1000 0 20
FE80::3

## Slide 7: IPv6 Show Commands
Routing protocol and Process ID (AS Number)
K values used in composite metric
EIGRP Administrative Distances
Interfaces enabled for this EIGRP for IPv6.
Branch-2# show ipv6 protocols
IPv6 Routing Protocol is "connected"
IPv6 Routing Protocol is "static
IPv6 Routing Protocol is "eigrp 100 "
EIGRP metric weight K1=1, K2=0, K3=1, K4=0, K5=0
EIGRP maximum hopcount 100
EIGRP maximum metric variance 1
Interfaces:
Serial0/0/0
Serial0/0/1
Redistributing: eigrp 100
Maximum path: 16
Distance: internal 90 external 170

## Slide 8: IPv6 Show Commands
Branch-2#show ipv6 route
(Output Omitted)
IPv6 Routing Table - 9 entries
C - Connected, L – Local, D - EIGRP, EX - EIGRP external
D 2001:DB8:ACAD:A::/64 [90/2170112]
via FE80::3, Serial0/0/1
D 2001:DB8:ACAD:B::/64 [90/2170112]
via FE80::3, Serial0/0/1
D 2001:DB8:ACAD:C::/64 [90/2170112]
via FE80::1, Serial0/0/0
D 2001:DB8:ACAD:D::/64 [90/2170112]
via FE80::1, Serial0/0/0
C 2001:DB8:CAFE::/127 [0/0]
via ::, Serial0/0/0
L 2001:DB8:CAFE::1/128 [0/0]
via ::, Serial0/0/0
C 2001:DB8:CAFE::2/127 [0/0]
via ::, Serial0/0/1
L 2001:DB8:CAFE::2/128 [0/0]
via ::, Serial0/0/1
L FF00::/8 [0/0]
via ::, Null0
Learned Networks
Directly Connected
Network Address
Interface Address

## Slide 9: Passive Interface Command
You can use the passive-interface command to control the advertisement of routing information.
The command enables the suppression of routing updates over some interfaces while it allows updates to be exchanged normally over other interfaces.
When used with EIGRP, it suppresses the exchange of hello packets between routers which will result in the loss of a neighbor relationship. Therefore, it is only used on interfaces where no routers are connected.
This stops not only routing updates from being advertised, but it also suppresses incoming routing updates.

## Slide 10: Passive Interface Configuration
Branch-1(config)# ipv6 router eigrp 100 Branch-1(config-rtr)# passive-interface g0/0 Branch-1(config-rtr)# passive-interface g0/1
Branch-1
S3
S4
PC-C
PC-D
2001:DB8:ACAD:C::1/64
2001:DB8:ACAD:D::1/64
2001:DB8:ACAD:C::2/64
2001:DB8:ACAD:D::2/64
G0/0
G0/1

## Slide 11: Show IPv6 Protocols Command
Branch-1#show ipv6 protocols
IPv6 Routing Protocol is "ND"
IPv6 Routing Protocol is "connected"
IPv6 Routing Protocol is "eigrp 100"
EIGRP-IPv6 Protocol for AS(100)
Metric weight K1=1, K2=0, K3=1, K4=0, K5=0
NSF-aware route hold timer is 240
Router-ID: 1.1.1.1
Topology : 0 (base)
Active Timer: 3 min
Distance: internal 90 external 170
Maximum path: 16
Maximum hopcount 100
Maximum metric variance 1
Interfaces:
Serial0/0/0
GigabitEthernet0/0 (passive)
GigabitEthernet0/1 (passive)
Redistribution:
None
Branch-1#

## Slide 12: IPv6 Summarization
Summarize Branch-3’s LANs into one summary address and then advertise to Branch-2.
Branch-3
S3
S4
PC-C
PC-D
2001:DB8:ACAD:A::/64
2001:DB8:ACAD:B::/64
2001:DB8:ACAD:A::1/64
2001:DB8:ACAD:B::1/64

## Slide 13: IPv6 Summarization
Summarized addresses are based on common bits in the network portion of the address.
The 2001:DB8:ACAD:A::/64 and the 2001:DB8:ACAD:B::/64 networks have 63-bits in common.
2001:DB8:ACAD:0000000000001010 = A
2001:DB8:ACAD:0000000000001011 = B
16-bits + 16-bits + 16-bits + 15-bits = 63 bits
Summary address would be 2001:DB8:ACAD:A::/63

## Slide 14: IPv6 Summarization Configuration
To advertise a summary address, issue the ipv6 summary-address eigrp AS address command and apply it to an interface where you would like the address to be advertised.
Branch-3(config)#int s0/0/1
Branch-3(config-if)#ipv6 summary-address eigrp 100 2001:DB8:ACAD:A::/63 5
Branch-3(config-if)#
%DUAL-5-NBRCHANGE: IPv6-EIGRP 100: Neighbor FE80::290:CFF:FE90:3E02 (Serial0/0/1) is up: new adjacency
Branch-2#show ipv6 route
(Output Omitted)
IPv6 Routing Table - 9 entries
C - Connected, L – Local, D - EIGRP, EX - EIGRP external
D 2001:DB8:ACAD:A::/63 [/2170112]
via FE80::3, Serial0/0/1
D 2001:DB8:ACAD:C::/64 [90/2170112]
via FE80::1, Serial0/0/0
D 2001:DB8:ACAD:D::/64 [90/2170112]
via FE80::1, Serial0/0/0

## Slide 15: Configuring IPv6 Default Route
Branch-2
2001:DB8:ACAD:C::1/64
2001:DB8:CAFE::/127
2001:DB8:ACAD:C::/64
S0/0/0
S0/0/1
Branch-3
S1
S2
Branch-1
2001:DB8:CAFE::2/127
S3
S4
PC-A
PC-B
PC-C
PC-D
2001:DB8:ACAD:D::/64
2001:DB8:ACAD:A::/64
2001:DB8:ACAD:B::/64
S0/0/1
S0/0/0
2001:DB8:ACAD:D::1/64
2001:DB8:ACAD:A::1/64
2001:DB8:ACAD:B::1/64
Lo0 2001:DB8:1::/64
Branch-2(config)# ipv6 route ::/0 lo0
Branch-2(config)# ipv6 router eigrp 100
Branch-2(config-rtr)# redistribute static

## Slide 16: Show ipv6 route command
Branch-1#show ipv6 route
IPv6 Routing Table - 12 entries
Codes: C - Connected, L - Local, S - Static, R - RIP, B - BGP
U - Per-user Static route, M - MIPv6
I1 - ISIS L1, I2 - ISIS L2, IA - ISIS interarea, IS - ISIS summary
O - OSPF intra, OI - OSPF inter, OE1 - OSPF ext 1, OE2 - OSPF ext 2
ON1 - OSPF NSSA ext 1, ON2 - OSPF NSSA ext 2
D - EIGRP, EX - EIGRP external
EX ::/0 [170/3449856]
via FE80::2, Serial0/0/0
D 2001:DB8:ACAD::/62 [5/2816]
via ::, Null0
C 2001:DB8:ACAD:C::/64 [0/0]
via ::, GigabitEthernet0/0
L 2001:DB8:ACAD:C::/128 [0/0]
via ::, GigabitEthernet0/0
Branch-2#show ipv6 route
IPv6 Routing Table - 11 entries
Codes: C - Connected, L - Local, S - Static, R - RIP, B - BGP
U - Per-user Static route, M - MIPv6
I1 - ISIS L1, I2 - ISIS L2, IA - ISIS interarea, IS - ISIS summary
O - OSPF intra, OI - OSPF inter, OE1 - OSPF ext 1, OE2 - OSPF ext 2
ON1 - OSPF NSSA ext 1, ON2 - OSPF NSSA ext 2
D - EIGRP, EX - EIGRP external
S ::/0 [1/0]
via ::, Loopback0
C 2001:DB8:1::/64 [0/0]
via ::, Loopback0
L 2001:DB8:1::/128 [0/0]
via ::, Loopback0
Notes: The default route was configured on Branch-2 and is displayed as a static route via the Loop back interface. Branch-1 displays the default route in its routing table as an external route. The only differences between IPv4 EIGRP and IPv6 EIGRP is (1) there is no asterisk shown on the device that creates the default route and it doesn’t list the gateway of last resort.